## Slide 1: Hardware Impairments in Large-scale MISO Systems
Emil Björnson‡*, Jakob Hoydis†, Marios Kountouris‡, and Mérouane Debbah‡
‡Alcatel-Lucent Chair on Flexible Radio and Department of Telecommunications, Supélec, France
†Bell Laboratories, Alcatel-Lucent, Stuttgart, Germany
*Signal Processing Lab, KTH Royal Institute of Technology, Sweden
Energy Efficiency, Estimation, and Capacity Limits

## Slide 2
Introduction

## Slide 3: Challenge of Network Traffic Growth
Data Dominant Era
  66% annual traffic growth
  Exponential increase!
Is this Growth Sustainable?
  User demand will increase
  Increased traffic supply only if network revenue is sustained!
Continuous Network Evolution
  What will be the next step?
Source: Cisco Visual Networking Index

## Slide 4: What Will Be Next Steps?
More Frequency Spectrum
  Scarcity in conventional bands: Use mmWave, cognitive radio
  Joint optimization of current networks (Wifi, 2G/3G/4G)
Improved Spectral Efficiency
  More antennas/km2 (space division multiple access)
What Limits the Spectral Efficiency?
  Propagation losses and transmit power
  Channel capacity
  Channel estimation accuracy (inter-user interference)
  Signal processing complexity
Our Focus:

## Slide 5: New Paradigm: Large Antenna Arrays
Remarkable New Network Architecture
  Deploy large arrays at macro base stations
Everything Seems to Become Better [1]
  Large array gain (improves channel conditions)
  Higher capacity (more antennas  more users)
  Orthogonal channels (little inter-user interference)
  Linear processing optimal (low complexity)
Properties Proved by Asymptotic Analysis
  Are conventional models applicable?
[1] F. Rusek, D. Persson, B. Lau, E. Larsson, T. Marzetta, O. Edfors, F. Tufvesson, “Scaling up MIMO: Opportunities and challenges with very large arrays,” IEEE Signal Process. Mag., 2013.

## Slide 6: Transceiver Hardware Impairments
Physical Hardware is Non-Ideal
  Oscillator phase noise
  Amplifier non-linearity
  IQ imbalance in mixers, etc.
Impact of Hardware Impairments
  Mismatch between the intended and emitted signal
  Distortion of received signal
  Limits capacity in high-SNR regime [2]
[2]: E. Björnson, P. Zetterberg, M. Bengtsson, B. Ottersten, “Capacity Limits and Multiplexing Gains of MIMO Channels with Transceiver Impairments,” IEEE Communications Letters, 2013
What happens in many-antennas regime?
Will everything still get better?

## Slide 7
Channel Model with Hardware Impairments

## Slide 8: Our Focus: Point-to-Point Channel
Scenario
  Base station (BS): antennas
  User terminal (UT): 1 antenna
  Channel vector
  Rayleigh fading
Time-Division Duplex (TDD)
  Channel reciprocity
  Uplink estimation of
  Downlink beamforming:
  User only needs to estimate

## Slide 9: Generalized Channel Model
Received Downlink Signal
[3]: T. Schenk, RF Imperfections in High-Rate Wireless Systems: Impact and Digital Compensation. Springer, 2008
Data Signal:
Noise:
Transmitter Distortion
Receiver Distortion
Distortion Noise per Antenna
Proportional to transmitted/received signal power
4 Prop. Constants: BS or UT, transmit or receive
Uplink:
Analogous
generalization

## Slide 10: Interpretation of Distortion Model
Gaussian Distortion Noise
  Independent between antennas
  Depends on beamforming
  Still uncorrelated directivity  Little in the signal dimension
Error Vector Magnitude (EVM)
  Quality of transceivers:
  LTE requirements: 0≤EVM≤0.17 (smaller  higher rates)
  Distortion will not vanish at high SNR!

## Slide 11
Main Contribution

## Slide 12: Contribution 1: Channel Estimation
New Linear MMSE Estimator
  Distortion noise is correlated with channel
  Normalized MSE is independent of
New Insights
Low SNR: Small difference
High SNR: Error floor
Error floor for i.i.d. channels:
Characterized by impairments!
Very different MSE but no need to change estimator

## Slide 13: Contribution 2: Capacity Limits
Explicit Capacity Bounds
  Upper: Channel is known
  Lower: LMMSE estimator
  Asymptotic limits:
New Insights
Capacity limited by UT hardware
: No impact of BS!
Large gain with moderate arrays
Quick convergence in
Upper/lower limits almost same

## Slide 14: Contribution 3: Energy Efficiency
Energy Efficiency in bits/Joule
  Capacity limited as
Theorem
Reduce power as
  Non-zero capacity as
New Insights
Power reduction from array gain
Same as with ideal hardware!
Capacity lower bounded by
EE grows without bound!

## Slide 15
Conclusions & Outlook

## Slide 16: Conclusions
New Paradigm: Large Antenna Arrays at BSs
  Promise high asymptotic spectral and energy efficiency
Physical Hardware has Impairments
  Creates distortion noise: Limits signal quality
  Limits estimation accuracy and prevents high capacity
  High energy efficiency is still possible!
Some Encouraging Results [4]
  Reduce BS hardware quality as
  SDMA is possible: Inter-cell interference drowns in distortions
[4] E. Björnson, J. Hoydis, M. Kountouris, M. Debbah, “Massive MIMO Systems with Non-Ideal Hardware: Energy Efficiency, Estimation, and Capacity Limits,” Trans. Information Theory, submitted arXiv:1307.2584

## Slide 17
Thank You for Listening!
Questions?
All Papers Available:
http://flexible-radio.com/emil-bjornson