## Slide 1: Optimal Resource Allocation in Coordinated Multi-Cell Systems
Emil Björnson
Post-Doc
Alcatel-Lucent Chair on Flexible Radio, Supélec, Gif-sur-Yvette, France
Signal Processing Lab., KTH Royal Institute of Technology, Stockholm, Sweden
EURECOM, 19 September 2013

## Slide 2: Biography: Emil Björnson
1983: Born in Malmö, Sweden
2007: Master of Science in Engineering Mathematics, Lund University, Sweden
2011: PhD in Telecommunications, KTH, Stockholm, Sweden
  Advisors: Björn Ottersten, Mats Bengtsson
  Visited EURECOM some weeks in 2008-2009
2012: Recipient of International Postdoc Grant from Sweden.
  Visit Supélec and Prof. Mérouane Debbah
  Topic: “Optimization of Green Small-Cell Networks”
  Research interests: Massive MIMO, Small cells, & Energy efficiency

## Slide 3: Book Reference
Seminar Based on Our Recent Book:
  270 pages
  E-book for free (from our homepages)
  Printed book: Special price $35, use link: https://ecommerce.nowpublishers.com/shop/add_to_cart?id=1595
  Matlab code is available online
Check out: http://flexible-radio.com/emil-bjornson
Optimal Resource Allocation in Coordinated Multi-Cell Systems
Research book by E. Björnson and E. Jorswieck
Foundations and Trends in Communications and Information Theory, Vol. 9, No. 2-3, pp. 113-381, 2013

## Slide 4: Outline
Introduction
  Multi-cell structure, system model, performance measure
Problem Formulation
  Resource allocation: Multi-objective optimization problem
Subjective Resource Allocation
  Utility functions, different computational complexity
Structural Insights
  Beamforming parametrization
Extensions to Practical Conditions
  Handling non-idealities in practical systems

## Slide 5
Section
Introduction

## Slide 6: Introduction
Problem Formulation (vaguely):
  Transfer information wirelessly to users
  Divide radio resources among users (time, frequency, space)
Downlink Coordinated Multi-Cell System
  Many transmitting base stations (BSs)
  Many receiving users
Sharing a Frequency Band
  All signals reach everyone!
Limiting Factor
  Inter-user interference

## Slide 7: Introduction: Multi-Antenna Single-Cell Transmission
Traditional Ways to Manage Interference
  Avoid and suppress in time and frequency domain
  Results in orthogonal single-cell access techniques: TDMA, OFDMA, etc.
Multi-Antenna Transmission
  Beamforming: Spatially directed signals
  Adaptive control of interference
  Serve multiple users: Space-division multiple access (SDMA)
Main difference from classical resource allocation!

## Slide 8: Introduction: From Single-Cell to Multi-Cell
Naïve Multi-Cell Extension
  Divide BS into disjoint clusters
  SDMA within each cluster
  Avoid inter-cluster interference
  Fractional frequency-reuse
Coordinated Multi-Cell Transmission
  SDMA in multi-cell: Cooperation between all BSs
  Full frequency-reuse: Interference managed by beamforming
  Many names: co-processing, coordinated multi-point (CoMP), network MIMO, multi-cell processing
Almost as One Super-Cell
  But: Different data knowledge, channel knowledge, power constraints!

## Slide 9: Basic Multi-Cell Coordination Structure
General Multi-Cell Coordination
  Adjacent base stations coordinate interference
  Some users served by multiple base stations
Dynamic Cooperation Clusters
Inner Circle : Serve users with data
Outer Circle : Suppress interference
Outside Circles:
  Negligible impact Impractical to acquire information Difficult to coordinate decisions
E. Björnson, N. Jaldén, M. Bengtsson, B. Ottersten, “Optimality Properties, Distributed Strategies, and Measurement-Based Evaluation of Coordinated Multicell OFDMA Transmission,” IEEE Trans. on Signal Processing, 2011.

## Slide 10: Example: Ideal Joint Transmission
All Base Stations Serve All Users Jointly = One Super Cell

## Slide 11: Example: Wyner Model
Abstraction: User receives signals from own and neighboring base stations
One or Two Dimensional Versions
Joint Transmission or Coordination between Cells

## Slide 12: Example: Coordinated Beamforming
One Base Station Serves Each User
Interference Coordination Across Cells
Special Case
Interference channel

## Slide 13: Example: Soft-Cell Coordination
Heterogeneous Deployment
  Conventional macro BS overlaid by short-distance small BSs
  Interference coordination and joint transmission between layers

## Slide 14: Example: Cognitive Radio
Secondary System Borrows Spectrum of Primary System
  Underlay: Interference limits for primary users
Other Examples
Spectrum sharing between operators
Physical layer security

## Slide 15: Resource Allocation: First Definition
Problem Formulation (imprecise):
  Select beamforming to maximize “system utility”
  Means: Allocate power to users and in spatial dimensions
  Satisfy: Physical, regulatory & economic constraints
Some Assumptions:
  Linear transmission and reception
  Perfect synchronization (whenever needed)
  Flat-fading channels (e.g., using OFDM)
  Perfect channel knowledge
  Ideal transceiver hardware
  Centralized optimization
Relaxed later on

## Slide 16: Multi-Cell System Model
Users: Channel vector to User from all BSs
Antennas at th BS (dimension of )
Antennas in Total (dimension of )
One System Model for Any Multi-Cell Scenario!

## Slide 17: Multi-Cell System Model: Dynamic Cooperation Clusters (2)
How are and Defined?
  This is User
  Beamforming: Data only from BS1:
  Effective channel: All BSs coordinate interference:
Example: Coordinated Beamforming

## Slide 18: Multi-Cell System Model: Power Constraints
Need for Power Constraints
  Limit radiated power according to regulations
  Protect dynamic range of amplifiers
  Manage cost of energy expenditure
  Control interference to certain users
General Power Constraints:
Weighting matrix
(Positive semi-definite)
Limit
(Positive scalar)
All at the same time

## Slide 19: Multi-Cell System Model: Power Constraints (2)
Recall:
Example 1, Total Power Constraint:
Example 2, Per-Antenna Constraints:

## Slide 20: Introduction: How to Measure User Performance?
Mean Square Error (MSE)
  Difference: transmitted and received signal
  Easy to Analyze
  Far from User Perspective?
Bit/Symbol Error Probability (BEP/SEP)
  Probability of error (for given data rate)
  Intuitive interpretation
  Complicated & ignores channel coding
Information Rate
  Bits per “channel use”
  Mutual information: perfect and long coding
  Anyway closest to reality?
All improves with SINR:
Signal
Interference + Noise

## Slide 21: Introduction: Generic Measure User Performance
Generic Model
  Any function of signal-to-interference-and-noise ratio (SINR):
  Increasing and continuous function
  For simplicity:
Example:
  Information rate:
Complicated Function
  Depends on all beamforming vectors
for User

## Slide 22
Section
Problem Formulation

## Slide 23: Problem Formulation
General Formulation of Resource Allocation:
Multi-Objective Optimization Problem
  Generally impossible to maximize for all users!
  Must divide power and cause inter-user interference

## Slide 24: Performance Region
Definition: Achievable Performance Region
  Contains all feasible combinations
  Feasible = Achieved by some under power constraints
2-User
Performance Region
Care about user 2
Care about user 1
Balance between users
Part of interest:
Pareto boundary
Pareto Boundary
Cannot improve for any user without degrading for other users
Other Names
Rate Region Capacity Region MSE Region, etc.

## Slide 25: Performance Region (2)
Can the region have any shape?
No! Can prove that:
  Compact set
  Normal set
Upper corner in region, everything inside region

## Slide 26: Performance Region (3)
  Some Possible Shapes
User-Coupling
Weak: Convex
Strong: Concave
Scheduling
Time-sharing for strongly coupled users
Select multiple points Hard: Unknown region

## Slide 27: Performance Region (4)
Utopia point (Combine user points)
Which Pareto Optimal Point to Choose?
  Tradeoff: Aggregate Performance vs. Fairness
Performance Region
Utilitarian point (Max sum performance)
Egalitarian point (Max fairness)
Single user point
Single user point
No Objective Answer
Utopia point outside of region
Only subjective answers exist!

## Slide 28
Section
Subjective Resource Allocation

## Slide 29: Subjective Approach
System Designer Selects Utility Function
  Describes subjective preference
  Increasing and continuous function
Examples:
Sum performance:
Proportional fairness:
Harmonic mean:
Max-min fairness:
Known as A Priori Approach
Select utility function before optimization
Put different weights to move between
extremes

## Slide 30: Subjective Approach (2)
Utility Function gives Single-Objective Optimization Problem:
This is the Starting Point of Many Researchers
  Although Selection of is Inherently Subjective Affects the Solvability
Pragmatic Approach
Try to Select Utility Function to Enable Efficient Optimization

## Slide 31: Complexity of Single-Objective Optimization Problems
Classes of Optimization Problems
  Different scaling with number of parameters and constraints
Main Classes
  Convex: Polynomial time solution
  Monotonic: Exponential time solution
  Arbitrary: More than exponential time
Approximations needed
Practically solvable
Hard to even approximate

## Slide 32: Classification of Resource Allocation Problems
Classification of Three Important Problems
  The “Easy” problem
  Weighted max-min fairness
  Weighted sum performance
We will see: These have Different Complexities
  Difficulty: Too many spatial degrees of freedom
  Convex problem only if search space is particularly limited
  Monotonic problem in general

## Slide 33: Complexity Example 1: The “Easy” Problem
Given Any Point
  Find beamforming that attains this point
  Minimize the total power
Convex Problem
  Second-order cone or semi-definite program
  Global solution in polynomial time – use CVX, Yalmip
  Alternative: Fixed-point iterations (uplink-downlink duality)
M. Bengtsson, B. Ottersten, “Optimal Downlink Beamforming Using Semidefinite Optimization,” Proc. Allerton, 1999.
A. Wiesel, Y. Eldar, and S. Shamai, “Linear precoding via conic optimization for fixed MIMO receivers,” IEEE Trans. on Signal Processing, 2006.
W. Yu and T. Lan, “Transmitter optimization for the multi-antenna downlink with per-antenna power constraints,” IEEE Trans. on Signal Processing, 2007.
E. Björnson, G. Zheng, M. Bengtsson, B. Ottersten, “Robust Monotonic Optimization Framework for Multicell MISO Systems,” IEEE Trans. on Signal Processing, 2012.
Total Power Constraints
Per-Antenna
Constraints
General Constraints

## Slide 34: Complexity Example 2: Max-Min Fairness
How to Classify Weighted Max-Min Fairness?
  Property: Solution makes the same for all
Line in direction ()
Solution is on this line

## Slide 35: Complexity Example 2: Max-Min Fairness (2)
Simple Line-Search: Bisection
  Iteratively Solving Convex Problems (i.e., quasi-convex)
Find start interval
Solve the “easy” problem at midpoint
If feasible:
  Remove lower half
  Else: Remove upper half
Iterate
Subproblem: Convex optimization
Line-search: Linear convergence
One dimension (independ. #users)

## Slide 36: Complexity Example 2: Max-Min Fairness (3)
Classification of Weighted Max-Min Fairness:
  Quasi-convex problem (belongs to convex class)
  Polynomial complexity in #users, #antennas, #constraints
  Might be feasible complexity in practice
T.-L. Tung and K. Yao, “Optimal downlink power-control design methodology for a mobile radio DS-CDMA system,” in IEEE Workshop SIPS, 2002.
M. Mohseni, R. Zhang, and J. Cioffi, “Optimized transmission for fading multiple-access and broadcast channels with multiple antennas,” IEEE Journal on Sel. Areas in Communications, 2006.
A. Wiesel, Y. Eldar, and S. Shamai, “Linear precoding via conic optimization for fixed MIMO receivers,” IEEE Trans. on Signal Processing, 2006.
E. Björnson, G. Zheng, M. Bengtsson, B. Ottersten, “Robust Monotonic Optimization Framework for Multicell MISO Systems,” IEEE Trans. on Signal Processing, 2012.
Early work
Main references
Channel uncertainty

## Slide 37: Complexity Example 3: Weighted Sum Performance
How to Classify Weighted Sum Performance?
  Geometrically: = opt-value is a line
Opt-value is unknown!
  Distance from origin is unknown
  Line  Hyperplane (dim: #user – 1)
  Harder than max-min fairness
  Non-convex problem

## Slide 38: Complexity Example 3: Weighted Sum Performance (2)
Classification of Weighted Sum Performance:
  Non-convex problem
  Power constraints: Convex
  Utility: Monotonic increasing/decreasing in beamforming vectors
  Therefore: Monotonic problem
Can There Be a Magic Algorithm?
  No, provably NP-hard (Non-deterministic Polynomial-time hard)
  Exponential complexity but in which parameters? (#users, #antennas, #constraints)
Z.-Q. Luo and S. Zhang, “Dynamic spectrum management: Complexity and duality,” IEEE Journal of Sel. Topics in Signal Processing, 2008.
Y.-F. Liu, Y.-H. Dai, and Z.-Q. Luo, “Coordinated beamforming for MISO interference channel: Complexity analysis and efficient algorithms,” IEEE Trans. on Signal Processing, 2011.

## Slide 39: Complexity Example 3: Weighted Sum Performance (3)
Are Monotonic Problems Impossible to Solve?
  No, not for small problems!
Monotonic Optimization Algorithms
  Improve Lower/upper bounds on optimum:
  Continue until
  Subproblem: Essentially weighted max-min fairness problem
H. Tuy, “Monotonic optimization: Problems and solution approaches,” SIAM Journal of Optimization, 2000.
L. Qian, Y. Zhang, and J. Huang, “MAPEL: Achieving global optimality for a non-convex wireless power control problem,” IEEE Trans. on Wireless Commun., 2009.
E. Jorswieck, E. Larsson, “Monotonic Optimization Framework for the MISO Interference Channel,” IEEE Trans. on Communications, 2010.
W. Utschick and J. Brehmer, “Monotonic optimization framework for coordinated beamforming in multicell networks,” IEEE Trans. on Signal Processing, 2012.
E. Björnson, G. Zheng, M. Bengtsson, B. Ottersten, “Robust Monotonic Optimization Framework for Multicell MISO Systems,” IEEE Trans. on Signal Processing, 2012.
Monotonic optimization
Early works
Polyblock
algorithm
BRB algorithm

## Slide 40: Complexity Example 3: Weighted Sum Performance (4)
Branch-Reduce-Bound (BRB) Algorithm
  Global convergence
  Accuracy ε>0 in finitely many iterations
  Exponential complexity only in #users ()
  Polynomial complexity in other parameters (#antennas, #constraints)

## Slide 41: Summary: Complexity of Resource Allocation Problems
Recall: All Utility Functions are Subjective
  Pragmatic approach: Select to enable efficient optimization
Good Choice: Any Problem with Polynomial complexity
  Example: Weighted max-min fairness
  Use weights to adapt to other system needs
Bad Choice: Weighted Sum Performance
  Generally NP-hard: Exponential complexity (in #users)
  Should be avoided – Sometimes needed (virtual queuing techniques)

## Slide 42: Summary: Complexity of Resource Allocation Problems (2)
Complexity Analysis for Any Dynamic Cooperation Clusters
  Same optimization algorithms!
  Extra characteristics can sometime simplify
  Multi-antenna transmission: More complex, higher performance
Ideal Joint Transmission
Coordinated Beamforming
Underlay Cognitive Radio

## Slide 43
Section
Structural Insights

## Slide 44: Parametrization of Optimal Beamforming
Complex Optimization Variables: Beamforming vectors
  Can be reduced to positive parameters
Any Resource Allocation Problem Solved by
  Priority of User :
  Impact of Constraint :
Lagrange multipliers of “Easy” problem

## Slide 45: Parametrization of Optimal Beamforming (2)
Geometric Interpretation:
Heuristic Parameter Selection
  Known to work remarkably well
  Many Examples (since 1995): Transmit Wiener filter, Regularized Zero-forcing, Signal-to-leakage beamforming, Virtual SINR beamforming, etc.
E. Björnson, M. Bengtsson, B. Ottersten, “Pareto Characterization of the Multicell MIMO Performance Region With Simple Receivers,” IEEE Trans. on Signal Processing, 2012.
Tradeoff
  Maximize signal vs. minimize interference
  Selfishness vs. altruism
  Hard to find optimal tradeoff
  Simple special case

## Slide 46
Section
Extensions to Practical Conditions

## Slide 47: Robustness to Channel Uncertainty
Practical Systems Operate under Uncertainty
  Due to estimation, feedback, delays, etc.
Robustness to Uncertainty
  Maximize worst-case performance
  Cannot be robust to any error
Ellipsoidal Uncertainty Sets
  Easily incorporated in system model
  Same classifications – More variables
  Definition:

## Slide 48: Distributed Resource Allocation
Information and Functionality is Distributed
  Local channel Knowledge and computational resources
  Only limited backhaul for coordination
Distributed Approach
  Decompose optimization
  Exchange control signals
  Iterate subproblems
Convergence to Optimal Solution?
  At least for convex problems

## Slide 49: Adapting to Transceiver Hardware Impairments
Physical Hardware is Non-Ideal
  Phase noise, IQ-imbalance, non-linearities, etc.
  Reduced calibration/compensation: Residual distortion remains!
  Non-negligible performance degradation at high SNRs
Model of Residual Transmitter Distortion:
  Additive noise
  Variance scales with signal power
Same Classifications Hold under this Model
  Enables adaptation: Much larger tolerance for impairments

## Slide 50
Summary

## Slide 51: Summary
Multi-Cell Multi-Antenna Resource Allocation
  Divide power between users and spatial directions
  Solve a multi-objective optimization problem
  Pareto boundary: Set of efficient solutions
Subjective Utility Function
  Selection has fundamental impact on solvability
  Multi-antenna transmission: More possibilities – higher complexity
  Pragmatic approach: Select to enable efficient optimization
  Polynomial complexity: Weighted max-min fairness
  Not solvable in practice: Weighted sum performance
Parametrization of Optimal Beamforming
Practical Extensions
  Channel uncertainty, Distributed optimization, Hardware impairments

## Slide 52: Main Reference: Our Book
Thorough Resource Allocation Framework
  More parametrizations and structural insights
  Guidelines for scheduling and forming clusters
  Matlab code distributed for algorithms
  Other Convex Problems and Optimization Algorithms:
Further Extensions:
  Multi-cast, Multi-carrier, Multi-antenna users, etc.
 | General
Sum Performance | NP-hard
Max-Min Fairness | Quasi-Convex
“Easy” Problem | Convex
 | General | Zero Forcing | Single Antenna
Sum Performance | NP-hard | Convex | NP-hard
Max-Min Fairness | Quasi-Convex | Quasi-Convex | Quasi-Convex
“Easy” Problem | Convex | Convex | Linear
Proportional Fairness | NP-hard | Convex | Convex
Harmonic Mean | NP-hard | Convex | Convex

## Slide 53
Thank You for Listening!
Questions?
All papers are available:
http://flexible-radio.com/emil-bjornson