## Slide 1: Massive MIMO Systems with Non-Ideal Hardware
Emil Björnson‡*
Joint work with: Jakob Hoydis†, Marios Kountouris‡, and Mérouane Debbah‡
‡Alcatel-Lucent Chair on Flexible Radio and Department of Telecommunications, Supélec, France
*Department of Signal Processing, KTH Royal Institute of Technology, Sweden
†Bell Laboratories, Alcatel-Lucent, Stuttgart, Germany
How does it Affect Energy Efficiency, Estimation, and Throughput?

## Slide 2: Outline
Introduction
  Challenge of traffic growth
  Massive multiple-input multiple-output (MIMO) systems
System Model with Hardware Impairments
  Non-linearities, phase noise, etc.
  How can it affect the system performance?
New Problems & New Results
  Channel estimation, capacity bounds, and energy Efficiency
  Some properties are changed by impairments, some are not
Conclusions & Outlook

## Slide 3
Introduction

## Slide 4: Challenge of Network Traffic Growth
Data Dominant Era
  66% annual traffic growth
  Exponential increase!
Is this Growth Sustainable?
  User demand will increase
  Growth = Increase in supply
  Increased traffic supply only if network revenue is sustained!
Is There a Need for Magic?
  No! Conventional network evolution
  What will be the next step?
Source: Cisco Visual Networking Index

## Slide 5: What are the Next Steps?
More Frequency Spectrum
  Scarcity in conventional bands: Use mmWave, cognitive radio
  Joint optimization of current networks (Wifi, 2G/3G/4G)
Improved Spectral Efficiency
  More antennas/km2 (space division multiple access)
Our Focus:

## Slide 6: Increasing the Spectral Efficiency
Multi-User Multiple-Input Multiple-Output (MIMO)
  Many multi-antenna base stations
  Many single-antenna users
  Share a frequency band
What Limits Spectral Efficiency?
  Inter-user interference
  Propagation losses, signal power
  Limited channel knowledge
  Limited coordination
Multi-Antenna Processing
  Spatial beamforming
  Theory: Low interference
  Practice: Hard to implement

## Slide 7: Potential Solution: Massive MIMO
New Remarkable Network Architecture
  Use large arrays at base stations: #antennas #users 1
  Hundreds of antennas, tenths of users
  Many degrees of freedom: Very narrow beamforming
  2013 IEEE Marconi Prize Paper Award:
  Thomas Marzetta, “Noncooperative Cellular Wireless with Unlimited Numbers of Base Station Antennas," IEEE Transactions on Wireless Communications, 2010.
Many names:
  Massive MIMO, Very large MIMO, Large-scale antenna systems, etc.

## Slide 8: Potential Solution: Massive MIMO (2)
Everything Seems to Become Better [1]
  Large array gain (improves channel conditions)
  Higher capacity (more antennas  more users)
  Orthogonal channels (little inter-user interference)
  Robustness to imperfect channel knowledge
  Linear processing near-optimal (low complexity)
[1] F. Rusek, D. Persson, B. Lau, E. Larsson, T. Marzetta, O. Edfors, F. Tufvesson, “Scaling up MIMO: Opportunities and challenges with very large arrays,” IEEE Signal Process. Mag., 2013.

## Slide 9: Where are the Gains Coming From?
Time-reversal processing = Matched filtering!
  Example: antennas
  Two user channels:
  Zero-mean i.i.d. entries
  Unit variance
  Matched filtering:
  Strong signal gain: as
  Interference vanish: as
What vanishes?
  Everything not matched to the channel: Inter-user interference, leakage from imperfect , noise, etc.

## Slide 10: Analytical and Practical Weaknesses
Main Properties Proved by Asymptotic Analysis
  Are conventional models applicable?
Simplified Channel Modeling
  Do we have rich scattering? Rayleigh fading?
  Prototypes and measurements partially confirm the results: Interference almost vanishes
Are there any Hardware Limitations?
  Low-cost equipment desirable for large arrays
  Theoretical treatment of hardware impairments is missing!

## Slide 11: Transceiver Hardware Impairments
Physical Hardware is Non-Ideal
  Oscillator phase noise, amplifier non-linearities, IQ imbalance in mixers, etc.
  Can be mitigated, but residual errors remain!
Impact of Residual Hardware Impairments
  Mismatch between the intended and emitted signal
  Distortion of received signal
  Limits spectral efficiency in high-power regime [2]
[2]: E. Björnson, P. Zetterberg, M. Bengtsson, B. Ottersten, “Capacity Limits and Multiplexing Gains of MIMO Channels with Transceiver Impairments,” IEEE Communications Letters, 2013
What happens in large- regime?
Will hardware impairments destroy anything?

## Slide 12
System Model with Hardware Impairments

## Slide 13: Our Focus: Point-to-Point Channel
Scenario
  Base station (BS): antennas
  User terminal (UT): 1 antenna
  Channel vector
  Rayleigh fading:
Properties of Covariance Matrix
  Bounded spectral norm as grows
  Due to law of energy conservation

## Slide 14: Our Focus: Point-to-Point Channel (2)
Time-Division Duplex (TDD)
  Uplink estimation overhead does not scale with
  Exploit channel reciprocity
  Estimation
  of
  User only needs
  to estimate
Downlink beamforming:
Uplink reception using

## Slide 15: How do Model Hardware Impairments?
Exact Characterization is Very Complicated
  Many types of impairments and mitigation algorithms
  Only the combined impact is needed!
Good and Simple Model of Residual Distortion
  Additive distortion noise
  From measurements: Independent between antennas Variance signal power at the antenna Gaussian distribution
  [3]: T. Schenk, “RF Imperfections in High-Rate Wireless Systems: Impact and Digital Compensation”. Springer, 2008
  [4]: M. Wenk, “MIMO-OFDM Testbed: Challenges, Implementations, and Measurement Results”. Hartung-Gorre, 2010

## Slide 16: Generalized System Model: Downlink
Conventional Model:
Generalized Model with Impairments:
  Distortion per antenna: Prop. to transmitted/received power
Proportionality constants

## Slide 17: Generalized System Model: Uplink
Conventional Model:
Generalized Model with Impairments:
  Distortion per antenna: Prop. to transmitted/received power
Proportionality constants

## Slide 18: Interpretation of Distortion Model
Gaussian Distortion Noise
  Independent between antennas
  Depends on beamforming
  Still uncorrelated directivity
Error Vector Magnitude (EVM)
  Quality of transceivers:
  EVM = Normalized standard deviation
  LTE requirements: (smaller  higher rates)
  Distortion will not vanish at high SNR!

## Slide 19
New Problems & New Results

## Slide 20: Result 1: Channel Estimation
Channel Estimation from Pilot Transmission
  Send known signal to observe the channel
Problem: Conventional Estimators Cannot be Used
  Relies on channel observation in independent noise
  Distortion noise is correlated with the channel
Contribution: New Linear MMSE Estimator
  Handles distortions that are correlated with channel

## Slide 21: Result 1: Channel Estimation (2)
MSE in i.i.d. case
New Insights
Low SNR: Small difference
High SNR: Error floor
Error floor in i.i.d. case:
Very different MSE but no need to change estimator
,

## Slide 22: Result 2: Capacity Behavior
Question: How is Throughput Affected?
  Conventionally: Capacity with #antennas or power
Contribution: New Characterization of UL/DL Capacities
  Upper bound: Channels are known, no interference
  Lower bound: Matched filtering, new LMMSE estimator, treat interference/channel uncertainty as noise
Asymptotic Upper Limits:

## Slide 23: Result 2: Capacity Behavior (2)
Bounded Capacity
  Small impact of BS impairments
  Other spatial signature!
New Insights
Capacity limited by UT hardware
: No impact of BS!
Major gains for up to
Minor gains above
Upper/lower limits almost same
Very different from ideal case!

## Slide 24: Result 3: Energy Efficiency
Energy Efficiency in bits/Joule
  Capacity limited as
Theorem
Reduce power as
  Non-zero capacity as
New Insights
Power reduction from array gain
Same scaling law as with ideal hardware!
EE grows without bound!
EE grows even for
,

## Slide 25: Result 3: Energy Efficiency (2)
Does an Infinite EE Make Sense?
  No! We only consider transmitted power, no circuit power
New Insights
EE maximized at finite
Depends on the circuit power that scales with
Large arrays become more feasible with time!
Impairments has minor impact!

## Slide 26: Result 4: Impact on Cellular Networks
Question: Impact of Hardware Impairments on a Network?
  Is there any fundamental difference?
Observation: Distortion Noise = Self-interference
  Self-interference is 20-30 dB weaker than signal
  Inter-user interference is negligible if weaker than this!
  Uncorrelated interference always vanish as !
Important Special Case: Pilot Contamination
  Necessary to reuse pilot sequences across cells
  Estimate is correlated with interfering pilot signals
  Corresponding interference will not vanish as !

## Slide 27: Result 4: Impact on Cellular Networks (2)
Contribution: Simple Inter-Cell Coordination Principle
  Same pilot to users causing weak interference to each other
  Other stronger interference: Vanishes as
New Insights
Pilot contamination is negligible if weaker than distortion
This condition can be fulfilled by pilot allocation!
Other interference vanishes asymptotically, as usual
PC<distortion
PC>distortion

## Slide 28
Conclusions & Outlook

## Slide 29: Conclusions
New Paradigm: Massive MIMO
  Potential: High spectral efficiency and energy efficiency
Physical Hardware has Impairments
  Creates distortion noise: Limits signal quality
  Limits estimation and prevents extraordinary capacity
  High energy efficiency is still possible!
  Pilot contamination becomes a smaller issue
Main Reference
  [5]: E. Björnson, J. Hoydis, M. Kountouris, M. Debbah, “Massive MIMO Systems with Non-Ideal Hardware: Energy Efficiency, Estimation, and Capacity Limits,” Submitted to IEEE Trans. Information Theory, arXiv:1307.2584

## Slide 30: Outlook
What is the optimal linear precoding?
  Rotated matched filter that reduces interference
  Problem: High complexity but can be approximated [6]
No Impact of Hardware Impairments at BSs as
  Hardware can be degraded: κ-parameters scaled as [5]
  Important property for practical deployments!
What is the Most Energy Efficient Deployment?
  Total EE is maximized by increasing the power with [7]
  [6]: A. Müller, A. Kammoun, E. Björnson, M. Debbah, “Linear Precoding Based on Truncated Polynomial Expansion,” Two parts, Submitted to JSTSP, Available on Arxiv.
  [7]: E. Björnson, L. Sanguinetti, J. Hoydis, M. Debbah, “Designing Multi-User MIMO for Energy Efficiency: When is Massive MIMO the Answer?,” Submitted WCNC 2014, Available on Arxiv.

## Slide 31
Thank You for Listening!
Questions?
All papers available:
http://flexible-radio.com/emil-bjornson