## Slide 1: Massive MIMO and Small Cells: Improving Energy Efficiency by Optimal Soft-Cell Coordination
Emil Björnson‡*, Marios Kountouris‡, and Mérouane Debbah‡
‡Alcatel-Lucent Chair on Flexible Radio and Department of Telecommunications, Supélec, France
*Signal Processing Lab, KTH Royal Institute of Technology, Sweden

## Slide 2
Introduction

## Slide 3: Challenge of Network Traffic Growth
Data Dominant Era
  66% annual growth of traffic
  How to achieve in a cost and energy efficient way?
Source: Unstrung Pyramid Research 2010
Source: Cisco Visual Networking Index 2013

## Slide 4: Is There a Need for Magic?
Still Room for Conventional Approaches
  Allocate more spectrum
  Network densification
More Frequency Spectrum
  Scarcity in conventional bands: Offload to mmWave bands, Cognitive radio
  Joint optimization of current networks (Wifi, 2G/3G/4G)
Network Densification
  Increased spatial reuse of spectrum
  More antennas/km2 (smaller cells, larger antenna arrays)
Our Focus:

## Slide 5: Two Approaches to Densification
Massive MIMO (multiple-input, multiple-output)
  Large antenna arrays: High beamforming resolution
  Deploy at macro base stations (BSs)
  Energy efficiency: Array gain + little interference
Small Cells
  Much traffic is localized and request by low-mobility users
  Deploy low-power small-cell access points (SCAs)
  Energy efficiency: Higher cell density  Smaller path losses

## Slide 6: Combination: Heterogeneous Network
Soft-Cell or Same-Cell Approach
  Overlay existing macro BS with SCAs
  BS: Guarantees coverage
  SCAs: Higher efficiency
  Transparent to users
Coordination Issue
  Control interference between BS/SCAs
  User-deployed SCAs: Only time/frequency division?
  Operator-deployed SCAs: Is spatial division possible?
Main Question:
What is achievable with perfect spatial coordination of BS and SCAs?

## Slide 7
Problem Formulation

## Slide 8: Can Massive MIMO + Small Cells Deliver?
Problem Formulation (vaguely)
  Minimize total power consumption
  Guarantee downlink quality-of-service at users (bits/s/Hz)
  Satisfy power constraints (very strict at SCAs)
How to Model Total Power Consumption?
  Dynamic part: Emitted power + Loss in amplifiers
  Static part: Powering of circuits related to each antenna
Predicted Impact of Massive MIMO and Small Cells:
Great decrease of dynamic part
Price: More hardware means higher static part
Will pros outweigh cons? What is a good practical deployment?

## Slide 9: System Model
Downlink Scenario
  One Macro BS: antennas
  SCAs: antennas each
  single-antenna users
  channel to user from BS () or th SCA
Received at user :
  Flat-fading subcarrier
Multiflow Linear Beamforming
  All BS and SCAs can send independent signals to all users:
  Joint non-coherent
From BS
From SCAs
Beamforming
Data signal
User Assignment
Automatic
and optimal
Noise

## Slide 10: System Model (2)
Power Consumption
  Dynamic part:
  Static part:
Power Constraints per BS/SCA:
Inefficiency of amplifiers
Number
of subcarriers
Circuit power/antenna
Weighting matrix
Positive limit
Examples
Per-antenna
Constraints
Per-BS/SCA constraints

## Slide 11: Problem Formulation
Optimization Problem:
Signal to Interf. and Noise Ratio:
What do we Seek?
  Solve this problem optimally
  Investigate which BS/SCAs will serve each user
  Compare different number of antennas and SCAs
Ultimate Bound
Ideal channel knowledge and backhaul
Quality of Service

## Slide 12
Analytic and Algorithmic Results

## Slide 13: Optimal Solution
Semi-Definite Reformulation ( ):
  Semi-definite program except for rank-constraint
QoS Targets
Theorem (Convex relaxation)
Suppose we drop the rank-constraints
Still always have a solution with
Hidden convexity
Optimal solution in polynomial time

## Slide 14: Automatic Transmitter-User Assignment
Conclusions:
  Most users served exclusively by one transmitter
  Spatial multiflow beamforming often not needed
  Transitions regions around SCAs
  Dynamic/self-organizing based on user load
Corollary
For each user in the optimal solution:
Served by only BS
Served by only th SCA
Served by a combination of BS/SCAs (whereof one has active power constraints, i.e., insufficient power)
No power constraints  No transition regions M. Bengtsson, “Jointly optimal downlink beamforming and base station assignment,” in Proc. IEEE ICASSP, 2001.

## Slide 15: Low-Complexity Algorithm
Optimal Solution in Polynomial Time
  Complexity scales cubic in number of antennas and users
  Modest complexity but infeasible for large arrays
Algorithm: Multiflow-RZF beamforming
All transmitters use regularized zero-forcing (RZF) as beamforming directions
SCAs send scalars of effective channel gains to BS
BS solves reduced-complexity linear problem:
BS informs SCAs on power allocation to users

## Slide 16
Simulation Examples

## Slide 17: Simulation Scenario
Channel Parameters
Rayleigh fading
(uncorrelated for SCAs and correlated for BS)
3GPP models for
shadow fading and path/penetration loss
600 subcarriers

## Slide 18: Can Massive MIMO + Small Cells Deliver?
Power Consumption with 2 bits/s/Hz per user:
Conclusions
  Both densification techniques work by themselves
  Combination makes even more sense
  Saturation can be observed (very parameter dependent)
  0-5% probability of multiflow beamforming

## Slide 19: Low-Complexity Coordination
What is Achievable in Practice?
  For different QoS constraints ()
Conclusions
  Proposed algorithm obtains large gain by using small cells
  Substantial gap is positive for practical applications
Practical performance

## Slide 20
Summary

## Slide 21: Summary
Improve Energy-Efficiency by Network Densification
  Massive MIMO – Large arrays at macro BSs
  Small Cells – New power-limited SCAs
  Does it make sense to combine them?
Spatial Soft-Cell Coordination
  Optimal multiflow beamforming: Convex problem
  Dynamic assignment of users to transmitters
  Exclusive assignment is usually optimal
Proof-of-Concept by Simulation
  Large energy savings due to decreased transmit power
  Usually compensates for increased static hardware power
  Low-complexity algorithms can bring great improvements

## Slide 22
Thank You for Listening!
Questions?
All Papers Available:
http://flexible-radio.com/emil-bjornson