## Slide 1: Circuit-Aware Design of Energy-Efficient Massive MIMO Systems
Emil Björnson‡*, Michail Matthaiou‡§, and Mérouane Debbah‡
‡Alcatel-Lucent Chair on Flexible Radio, Supélec, France
*Dept. Signal Processing, KTH, and Linköping University, Sweden
§ECIT, Queen’s University Belfast, U.K., and S2, Chalmers, Sweden

## Slide 2: A Conjecture for Massive MIMO
”Massive MIMO can be built with inexpensive, low-power components.”
“Massive MIMO reduces the constraints on accuracy and linearity of each individual amplifier and RF chain.”
“Massive MIMO for next generation wireless systems,” by E. G. Larsson, O. Edfors, F. Tufvesson and T. L. Marzetta, in IEEE Communications Magazine, 2014.
Is this true?
There are some indicative results in the literature [3],[7]
In this paper we provide a more comprehensive answer!

## Slide 3
Introduction

## Slide 4: Introduction: Massive MIMO
Multi-Cell Multiple-Input Multiple-Output (MIMO)
  Cellular system with cells
  Base stations (BSs) with antennas
  single-antenna users per cell
  Share a flat-fading subcarrier
  Beamforming: Spatially directed transmission/reception
Massive MIMO
Large arrays: e.g.,
Very narrow beamforming
Often: (not necessary!)
Little interference leakage

## Slide 5: What is New with Massive MIMO?
Many Antenna Elements?
  We already have many antennas!
  LTE-A:
  But only 12-24 antenna ports!
MIMO with Many Antenna Ports
  Duplicate hardware components
3 sectors, 4 vertical arrays/sector, 20 antennas/array
Image source: gigaom.com
On Each Uplink Receiver Chain
Several Filters,
Low-Noise Amplifier (LNA), Mixer,
Analog-to-Digital Converter (ADC)
And: 1 or Local Oscillators (LOs)

## Slide 6: Hardware-Constrained Base Stations
Can We Afford High-Quality Components?
  Does cost and circuit power increase linearly with ?
  How does cheaper and more energy-efficient hardware affect massive MIMO?
Real Hardware is Imperfect (Non-Ideal)
  Less Expensive, more energy-efficient = More imperfect
  Partial answers given in this paper
  Noise amplification
  Quantization noise
  Phase noise
Modeling of Imperfections
Essential to understand impact of low-quality low-power components!

## Slide 7
System Model

## Slide 8: Basic Assumptions
Channel Assumptions
  Channels from cell to cell :
  Rayleigh fading:
Block Fading
  Fixed realizations for channel uses (coherence block)
Uplink Signals
  From UE , cell : with power
  Used for both pilot and data
  Signals from cell :

## Slide 9: Conventional and New Uplink Model
Received in Cell :
New Generalized Model:
  Thermal noise (variance )
  Signal from UEs in cell
  Channels from UEs in cell
Phase Drift
Rotates phases by Wiener process:
Distortion Noise
Proportional to received signal:
Receiver Noise

## Slide 10: Characterization: Hardware Imperfections
Model has 3 Parameters:
  Ideal hardware:
  Circuit power roughly prop. to and
Phase Drifts
  Variance of innovations
  Source: Phase noise in LOs
  One LO: Equal drifts on all antennas
  separate LOs: All drifts are independent
Distortion Noise
  Error vector magnitude (EVM) =
  Source: Quantization noise (with automatic gain control)
Receiver Noise
  Noise amplification factor (of thermal noise)
Main Question
How do
affect the performance in massive MIMO?

## Slide 11
Overview of Analytic Contributions

## Slide 12: Channel Estimator and Predictor
Effective Channel:
  Time-varying: Channel fixed but phase drifts
  Distortion noise correlated with channels
Pilot Sequence: User in cell :
Lemma 1
Linear minimum mean squared error (LMMSE) estimate of :
Error covariance:
  Need new estimator/ predictor

## Slide 13: Achievable User Rates
New Lower Bound on Rate at UE in cell :
  Time-varying receive combining:
  Signal-to-interference-and-noise ratio (SINR):
  Receiver Noise
  Signal Power
  Distortion Noise
  Inter-User Interference
Lemma 2
Closed form expressions for all expectations for
(maximum ratio combining (MRC))

## Slide 14: Asymptotic Limit and Scaling Law
What Happens to User Rates as ?
  Distortion noise and receiver noise vanish!
  Phase drifts remain: Reduce signal and interference power
Example: Rates with MRC and SLOs
  Inner product of pilot sequences
Lemma 3 (Scaling Law on Hardware Imperfections)
Substitute
If exponents are selected as
then the SINRs stay non-zero as

## Slide 15: Interpretation of Scaling Law
Hardware can be Gradually Degraded as
  Increase Distortion/Receiver Noise Variances ( as
  Example: fewer quantization bits (in ADC) dB higher noise figure (in LNA)
  Circuit power: Inversely proportional to  Decrease as
  Increase Phase Drift Variance with SLOs as
  Example: Increase phase noise variance or handle larger
  Additive distortions
  Multiplicative distortions
Massive MIMO Systems with Hardware-Constrained Base Stations, E. Björnson (Supélec, KTH)
15
Lemma 3 (Scaling Law on Hardware Imperfections)
Substitute
If exponents are selected as
then the SINRs stay non-zero as

## Slide 16
Numerical Example

## Slide 17: Simulation Scenario
Main Characteristics
  , uniform UE distribution in 8 virtual sectors (> 35 m)
  Typical 3GPP pathloss model
Assumptions
Pilot sequences:
Coherence block:
Number of antennas:

## Slide 18: Area Sum Rates
Three Cases
  Ideal Hardware
  Fixed imperfect hardware: (8 bit ADCs, 2 dB noise figure, phase noise variance )
  Variable Imperfect hardware: As in Lemma 3 for CLO/SLOs
Observations
Manageable impact if scaling laws are fulfilled
Otherwise: Drastic reduction
Separate Oscillators
Can tolerate much more phase noise!

## Slide 19
Conclusions

## Slide 20: Conclusions
Massive MIMO with Hardware Imperfections at BSs
  Massive MIMO is resilient to such imperfections
  Distortion noise and amplified receiver noise vanish as
  Phase drifts remains but do not get worse
Scaling Law for Hardware Imperfections
  Distortion/receiver noise variance can increase as (: 10 dB higher noise figure, 1.6 fewer quant. bits)
  Phase drift variance with SLOs increases as
Important Conclusions for Massive MIMO
Conjecture from IEEE Communications Magazine is true!
Can be deployed with inexpensive and energy-efficient hardware!
Circuit-aware design: Total circuit power increase as instead of

## Slide 21
Thank You for Listening!
Questions?
Also check out:
E. Björnson, M. Matthaiou, M. Debbah, “Massive MIMO Systems with Hardware-Constrained Base Stations,” Proceedings of ICASSP, Florence, Italy, May 2014.