## Slide 1: Robust Monotonic Optimization Framework for Multicell MISO Systems
Emil Björnson1, Gan Zheng2, Mats Bengtsson1, Björn Ottersten1,2
1 Signal Processing Lab., ACCESS Linnaeus Centre, KTH Royal Institute of Technology, Sweden
2 Interdisciplinary Centre for Security, Reliability and Trust (SnT), University of Luxembourg, Luxembourg
Published in IEEE Transactions on Signal Processing, vol. 60, no. 5, pp. 2508-2523, May 2012

## Slide 2: Introduction
Downlink Coordinated Multicell System
  Many multi-antenna transmitters/BSs
  Many single-antenna receivers
Sharing a Frequency Band
  All signals reach everyone!
  Limiting factor: co-user interference
Multi-Antenna Transmission
  Spatially directed signals
  Known as: Beamforming/precoding

## Slide 3: Problem Formulation
Typical Problem Formulations:
Bad News: NP-hard problem (treating co-user interference as noise)
  High complexity: Approximations are required in practice
  Common approach: Propose an approx. and compare with old approxs.
  Can we solve it optimally for benchmarking?
maximize System Utility
Precoding for all users
subject to Power Constraints
Weighted sum of user performance,
Proportional fairness,
etc.
Limited total power,
Limited power per transmitter,
Limited power per antenna
Z.-Q. Luo and S. Zhang, “Dynamic spectrum management: Complexity and duality,” IEEE Journal of Sel. Topics in Signal Processing, 2008.
(1)

## Slide 4: Contribution & Timeliness
Main Contribution
  Propose an algorithm to solve Problem (1) optimally
  Timely: Several concurrent works
Differences from Concurrent Works
  Use state-of-the-art branch-reduce-and-bound (BRB) algorithm
  Handle robustness to channel uncertainty
  Arbitrary multicell scenarios and performance measures
W. Utschick and J. Brehmer, “Monotonic optimization framework for coordinated beamforming in multicell networks,” IEEE Trans. on Signal Processing, vol. 60, no. 4, pp. 1899–1909, 2012.
L. Liu, R. Zhang, and K. Chua, “Achieving global optimality for weighted sum rate maximization in the K-user Gaussian interference channel with multiple antennas,” IEEE Trans. on Wireless Communications, vol. 11, no. 5, pp. 1933–1945, 2012.
BRB Algorithm: H. Tuy, F. Al-Khayyal, and P. Thach, “Monotonic optimization: Branch and cut methods,”, Springer, 2005.

## Slide 5
System Model

## Slide 6: Many Different Multicell Scenarios
Ideal Joint Transmission
Coordinated Beamforming
(Interference channel)
Underlay Cognitive Radio
One Generic BS Coordination Model
Scenario given by a diagonal matrix
: BSs sending data to User
: BSs coordinating interf. to User 𝑘
Large distance: Negligible interf.
Multi-Tier Coordination

## Slide 7: Multicell System Model
Users: Channel vector to User from all BSs
Antennas at th BS (dimension of )
Antennas in Total (dimension of )

## Slide 8: Robustness to Uncertain Channels
Practical Systems Operate under Uncertainty of
  Due to Estimation, Feedback, Delays, etc.
  Robustness: Maximize worst-case performance
Uncertainty Sets at BSs
  Estimation motivates ellipsoidal sets
  Definition:

## Slide 9: User Performance
Error in Signal Equalization at User :
  Worst-case mean squared error (MSE):
Generic User Performance
  Any function of worst-case MSE:
  Monotonic decreasing and continuous function
  For simplicity:
  Example: Guaranteed Information Rate

## Slide 10: Robust Performance Region
Limited Power
  Physical constraints, regulations, cost, etc.
  general power constraints:
Robust Performance Region
  All feasible
  Good points: On upper boundary
  Different system utilities = different points
  Unknown shape: Can be non-convex
  Lemma 1: Region is compact and normal
Weighting matrix
(Positive semi-definite)
Limit
(Positive scalar)
2-User
Performance Region

## Slide 11: Problem Formulation
Find Optimal Solution to Detailed Version of (1):
  For monotonic increasing system utility function :
    Sum performance:
    Proportional fairness:
    Max-min fairness:
Equivalent to Search in Performance Region:
(2)

## Slide 12
Special Case:
Fairness-Profile Optimization

## Slide 13: Fairness-Profile Optimization
Consider Special Case of (2):
  Called: Fairness-profile optimization
  Generalization of max-min fairness
Simple Geometric Interpretation
  Can we search on the line?
  Region is unknown
Minimal performance of User
Fairness-profile
(Portion to User )

## Slide 14: Fairness-Profile Optimization (2)
How to Check if a Point on the Line is Feasible?
  Proof: Based on S-lemma in robust optimization
Theorem 1
A point is in the region if and only if the following convex feasibility problem is feasible:

## Slide 15: Fairness-Profile Optimization (3)
Simple Line-Search: Bisection
  Line-search: Linear convergence
  Sub-problem: Feasibility check
  Works for any number of user
Bisection Algorithm
Find start interval
Check feasibility of midpoint using Theorem 1
If feasible:
  Remove lower half
  Else: Remove upper half
Iterate
Summary
Fairness-profile problem solvable in polynomial time!

## Slide 16
BRB Algorithm

## Slide 17: Computing Optimal Strategy: BRB Algorithm
Solve (2) for Any System Utility Function
  Systematic search in performance region
  Improve lower/upper bounds on optimum:
Branch-Reduce-and-Bound (BRB) Algorithm
  Cover performance region with a box
  Divide the box into two sub-boxes
  Remove parts with no solutions in
  Search for solutions to improve bounds
  Continue with sub-box with largest value
End when bounds
are tight enough:
Accuracy

## Slide 18: Computing Optimal Strategy: Example
Theorem 2
  Guaranteed convergence to global optimum
  Accuracy ε>0 in finitely many iterations
  Exponential complexity only in #users ()
  Polynomial complexity in other parameters (#antennas, #constraints)

## Slide 19
Numerical Examples

## Slide 20: Example 1: Convergence
Convergence of Lower/Upper Bounds
  Compared with Polyblock algorithm (proposed only for perfect CSI)
  Scenario: 2 BSs, 3 antennas/BS, 2 users, perfect channel knowledge
  Plot relative error in lower/upper bounds (sum rate optimization)
Observations
  BRB algorithm has faster convergence
  Lower bound converges rather quickly

## Slide 21: Example 2: Benchmarking
Evaluate Robustness of Heuristic Beamforming
  Heuristic 1: Classical zero-forcing beamforming
  Heuristic 2: New interference-constrained beamforming
  Scenario: 2 BSs, 3 antennas/BS, 6 users
  Spherical uncertainty sets: Radius and channel variance
Observations
  Close to optimal at high SNR and small
  Highly suboptimal for large
  Heuristic 2 somewhat better for large

## Slide 22
Conclusion

## Slide 23: Conclusion
Maximize System Utility in Coordinated Multicell Systems
  NP-hard problem in general: Only suboptimal solutions in practice
  How can we truly evaluate a suboptimal solution?
Robust Monotonic Optimization Framework
  Solves a wide range of system utility maximizations
  Handles channel uncertainty and any monotone performance measures
  Subproblem: Fairness-profile optimization (FPO) = polynomial time
  BRB algorithm: Solves finite number of FPO problems
  Generalization: Problems where feasibility of a point is checked easily
Do you want to test it?
  Download Matlab code from the book “Optimal Resource Allocation in Coordinated Multi-Cell Systems” by E. Björnson & E. Jorswieck
  Based on CVX package by Steven Boyd et al.

## Slide 24
Thank you for your attention!
Questions?

## Slide 25
Backup Slides

## Slide 26: Generic Multicell Setup
Many examples:
  Interference channel
  Arbitrary overlapping cooperation clusters
  Global joint transmission
  Underlay cognitive radio, etc.
Dynamic Cooperation Clusters
Inner Circle : Serve users with data
Outer Circle : Suppress interference
Outside Circles:
  Negligible impact – modeled as noise
26

## Slide 27: Dynamic Cooperation Clusters
How are and Defined?
  Consider User :
Interpretation:
  Block-diagonal matrices
  has identity matrices for BSs that send data
  has identity matrices for BSs that can/should coordinate interference

## Slide 28: Dynamic Cooperation Clusters (2)
Example: Coordinated Beamforming
  This is User
  Beamforming: Data only from BS1:
  Effective channel: Interference from all BSs:

## Slide 29: Power Constraints: Examples
Recall:
Example 1, Total Power Constraint:
Example 2, Per-Antenna Constraints:
Example 3, Control Interference to User

## Slide 30: Performance Region: Shapes
Can the region have any shape?
No! Can prove that:
  Compact set
  Normal set
Upper corner in region, everything inside region

## Slide 31: Performance Region: Shapes (2)
  Some Possible Shapes
User-Coupling
Weak: Convex
Strong: Concave